## Slide 1: A Novel Aliasing vs Non Aliasing Audio Dataset for Always-On IoT Microphone Experimentation
Jack Adiletta*
Professor Bashima Islam*, Professor Shiwei Fang**
Graduate Students: Khan Hossain*, Matthew Reynolds***
WPI BASH Lab
ACM BuildSys 2025, November 19th
*WPI, **Augusta University, ***Colombia University

## Slide 2: Agenda
Problem Space
Aliasing vs Non Aliasing Audio
Generating Aliasing Audio
Errors Generating Aliasing and Non Aliasing Audio
Audio Encoding Techniques
Dataset Structure
Conclusion
Notes: Neural Network symbol
Fourier series symbol
Op amp symbol
Improve spacing
Verbally say the research includes mathematical analysis, circuit design and analysis, data science and machine learning

## Slide 3: Why an Audio Aliasing Dataset is Useful
There is a proliferation of microphones in buildings, cars, urban environments
It is beneficial to have lower sample rate (power / bandwidth, storage)
An aliasing vs non aliasing dataset can be used to optimize the sample rate of a microphone for lowest power/bandwidth/storage without aliasing.
First publicly available dataset to include deliberate aliasing vs non aliasing audio

## Slide 4: What is Aliasing Audio?
Nyquist Frequency: Twice the highest frequency of a signal to sample [2]
Aliasing: when audio is sampled at less than the Nyquist Frequency [5]
Aliasing occurs because higher frequencies cannot be represented by a lower sample rate which imparts distortion, audio artifacts, or noise.

## Slide 5: Aliasing Audio Examples
A 10 Hz Sine Wave Sampled at 8 Hz
(Aliasing)
A 10 Hz Sine Wave Sampled at 25 Hz
(Non Aliasing)
Dog Bark Sampled at 1 kHz
(Aliasing)
Dog Bark Sampled at 22 kHz
(Non Aliasing)

## Slide 6: Generating a Dataset of Aliasing & Non Aliasing Audio
Example 8 kHz
Process repeated for 1 kHz, 2 kHz, 4 kHz, 16 kHz, 22 kHz
Audio sources are:
Urbansound 8K [3]
ESC 50 [4]
MAVD [5]

## Slide 7: Generating Aliasing & Non Aliasing Audio
1s Audio Recording
(contains frequencies above 4 kHz)
Low pass filter at 4 kHz
(remove frequencies above 4 kHz)
Playback is aliasing
Playback is non aliasing!
Sample at 8 kHz
Sample at 8 kHz

## Slide 8: Errors Generating Aliasing & Non Aliasing Audio
Audio Recording
Sample at 8 kHz
Playback is silent?
Three environmental sound datasets
Urban Sound 8K ~4s
ESC 50 ~5s
MAVD > 1 minutes
Break recording into 1 second chunks
Remove recordings with a mean square power less than a threshold

## Slide 9: Fast Fourier Transform
[6]

## Slide 10: Errors Generating Aliasing Audio
Audio Recording
Sample does not contain frequencies above 4 kHz
Sample at 8 kHz
Playback is loud
but not aliasing?
Remove recordings without high frequencies
Fast Fourier Transform [3]

## Slide 11: Encoding Audio Data

## Slide 12: Representing Audio for AI / ML Analysis
Fast Fourier Transform? [6]
Does not capture changes in frequencies over time!
Short Term Fourier Transform (STFT)

## Slide 13: Visual Representation of Aliasing Audio (AC unit)
Unfiltered – Aliasing
Filtered – Non Aliasing
Note: Sampled at 4 kHz

## Slide 14: Dataset Structure
Processed_Files/
DS_U8K/ # urbansound 8K
DS_ESC/ # ESC 50
DS_ZEN/ # MAVD Dataset
22000/
16000/
8000/
4000/
2000/
1000/
train/ # 80%
validation/ # 10%
test/ # 10%
filtered/
unfiltered/
Contains 97,891 unique 1-second aliasing and non aliasing samples
Processed into AI/ML friendly STFTs or MFCCs
U8K and ESC50 data samples contain original class (dog bark, AC) in file title

## Slide 15: Conclusion and Contributions:
Developed Novel Aliasing / Non Aliasing Audio Generation Method
  Filter audio to generate non aliasing samples
Implemented two audio encoding techniques
  Audio sampled at six sample rates
Published Compressed Dataset
  Available via Zenodo

## Slide 16
Thank you!
Questions?

## Slide 17: References
[1] Fabian Esqueda, Stefan Bilbao, and Vesa Valimaki. 2016. Aliasing reduction in clipped signals. IEEE Transactions on Signal Processing 64, 20 (2016), 52555267.doi:10.1109/tsp.2016.2585091
[2] Bogdan Mihai. 2009. Sampling rate and aliasing on a virtual laboratory. Journal of Electrical and Electronics Engineering 2 (10 2009).
[3] Justin Salamon, Christopher Jacoby, and Juan Pablo Bello. 2014. UrbanSound8K.
[4] Karol J. Piczak. 2015. ESC: Dataset for Environmental Sound Classification. In Proceedings of the 23rd Annual ACM Conference on Multimedia (Brisbane, Australia,2015-10-13). ACM Press, 1015–1018. doi:10.1145/2733373.2806390
[5] Pablo Zinemanas, Pablo Cancela, and Martín Rocamora. 2019. MAVD: A Dataset for Sound Event Detection in Urban Environments. In Proceedings of the DCASE2019 Workshop. New York, USA, 25–26.
[6] O. Trekhleb, Fourier Decomposition. DEV Community, 2021.

## Slide 18
Backups

## Slide 19: Visual Representation of Aliasing Audio
Unfiltered – Aliasing
Filtered – Non Aliasing
Note: Sampled at 22 kHz